## Slide 1: MAGNETISM
MAGNETISM?
MAGNETIC MATERIALS?
LINES OF FORCE-FLUX?
INDUCTION?
BLUE/RED POLES?

## Slide 2: Ship’s compass- ‘STANDARD’ or MAGNETIC
Mariner’s Compass– DRY CARD, WET CARD
A Magnetic Marvel.
ERROR- due to MAGNETISM (GEO-earth and Ship’s material)
GEO causes VARIATION (EAST/WEST) ; Material (ferro-MILD STEEL) gives DEVIATION (EAST/WEST)
ALGEBRIC SUM OF VARIATION ,DEVIATION IS COMPASS ERROR
ERROR IS NAMED ‘EAST’ OR ‘WEST’

## Slide 3: MAGNET-LOADSTONE
PROPERTIES OF FREELY SUSPENDED MAGNET
END-ON POSITION
BROAD SIDE ON POSITION

## Slide 4: GEO MAGNETISM
GEO (Earth) is a magnet. magnetic Poles, magnetic Equator
It’s magnetic field- 3 Elements.
TOTAL FORCE-’I’ or ‘F’– resultant of ‘H’ and ‘Z’ forces
DIP/INCLINATION
VARIATION/DECLINATION
SECULAR CHANGE/TRANSIENT CHANGES

## Slide 5: Ship’sPermanent magnetic field—constant forces
Horizontal component-fore/aft direction—’P’ Force
+ if field works towards Bow, - if towards Stern
Horizontal component-athwartship direction-’Q’ Force
+ if towards Starboard, - if towards Port
Vertical component—’R’ force
+ if towards down, - if upwards
Forces are neither affected by course change nor with change of latitude.
But their effect on compass changes with change in course and/or latitudes.

## Slide 6: Ship’s Induced Magnetism
Caused by ship’s soft iron parts
By ‘H’ and by ‘Z’ [horizontal and vertical components of total force’I’
rules of 9 rods--imaginary

## Slide 7: COMPASS WORK
PERMANENT MAGNETISM
INDUCED MAGNETISM
5 COEFFICIENTS—’A’ ‘B’ ‘C’ ‘D’ ‘E’—it is not a force; measured in degrees.
3 TYPES OF DEVIATIONS CAUSED BY COEFFICIENTS-
CONSTANT [A], SEMICIRCULAR [B/C], QUADRANTAL [D/E]
Total Deviation= A+ Bsin co+ C Cos co+D Sin 2 co + E Cos 2 co

## Slide 8: Coefficient ‘A’
Definition- constant deviation caused by induced magnetism
REAL--causes
APPARENT-causes

## Slide 9: Coefficient ‘B’
Permanent-PB- due to hard iron—force /P’
Induced- iB– due to soft iron—EARTH FORCE
Correction– ‘LIKE CURES LIKE’ AS BELOW
FORE AND AFT Magnets and FLINDER’S BAR

## Slide 10: Coefficient ‘C’
Permanent- PC—Hard iron—’force-Q’
Induced- iC—Soft iron--- EARTH FORCE
Correction- LIKE CURES LIKE AS BELOW
ATHWART SHIP MAGNETS and FLINDER’S BAR

## Slide 11: Coefficient ‘D’
No permanent magnetism as the cause of effect.
It is due to induced magnetism.
Transverse beams are more than fore and aft placed girders on ships,
so merchant ships have +D.
Correction by Soft iron correctors-’quadrantal correctors’

## Slide 12: Coefficient ‘E’
Caused due to induced magnetism of horizontal soft irons situated symmetrically along 45 degree line through compass position.
Deviation due to coefficient ‘D’ and ‘E’ does not get affected ,if latitude changes. They are impacted only by change of course.
Correction—by S.I. Correctors –placed diagonally. For ‘D’ and ‘E’ together – single set of correctors are accordingly placed on angle from athwart ship position [‘D’ is corrected first].
Tan 2x [angle]= E/D
Maximum deviation due to D/E= √D²+E² [NE/SW or on NW/SE]

## Slide 13: Heeling Error
It is difference in deviation between that when the ship is upright and that when heeled on the same course.
Caused due to HORIZONTAL COMPONENT OF OBLIQUE FIELD –as ship heels.
Permanent HE= Due to ‘R’
Induced H/E = ‘k’ , ‘e’ , ‘g’ , ‘c’ rods
Correction- use of vertical force instrument and H.E magnets

## Slide 14: GAUSSIN AND RETENTIVE ERRORS
Caused due to sub-permanent magnetism
RETENTIVE ERROR-seen when vessel alters course after long haul on one course.
GAUSSIN ERROR—Lenz’s law & Hysteresis
Error is seen when ship is swinging

## Slide 15: DIRECTIVE FORCE
This is the force which enables any magnetic body to point to magnetic north---denoted by ‘H’.
It is impacted by ‘P’, ‘Q’, ‘c rod’, ‘a rod’ , ‘e rod’.
Lambda 1= Mean DF at compass position/ H, VALUE generally less than 1 on a ship.
For a correction made for’D’ Lambda is named as ‘LAMBDA 2’.
Both above can be measured by Horizontal vibrating needle

## Slide 16: COMPASS CORRECTION- D.F Method
BY Kelvin Deflector
BY Deviascope deflector
BY Vibrating needle
All above are DIRECTIVE FORCE METHODS FOR COMPASS ADJUSTMENT

## Slide 17: COMPASS CORRECTION- Deviation method
Analysis method & shorter method- for full correction when compass is first installed, or major alteration of structure has taken place for ship.
Tentative method –only for readjustment –once a year; routine
or after carrying iron cargo. Deviation curve to be made and to be available as record—on board.

## Slide 18: IMO PERFORMANCE STANDARDS
Performance standards are laid down by IMO for compass card, material, constructional errors, corrective devices, construction and siting.
Precautions are also laid down while swinging ship for adjustment/correction of compass.